## Slide 1
LAB 5
Traffic Light controller, Finite state machines, c programming

## Slide 2
Objectives
Create a Traffic Light controller
Model your program’s flow using a finite state machine
Implement the finite state machine in C using Structs
Design the circuit for your traffic light

## Slide 3
details
Absolutely no conditionals are allowed such as do-while, while-loop, if-then, or for-loops
For some reason using SYSTCTL_RCGCGPIO_R will not properly initialize your clocks, so we must use SYSCTL_RCGC2_R (legacy register) for this lab instead
To flash the warning pedestrian light, you will need to cycle between a few states
I strongly suggest doing all debugging on the hardware and avoiding usage of the grader (grader software outdated for this lab, issues with SysTick delay on simulator)
We are following American traffic light convention – red means stop, yellow means slow down, green means go

## Slide 4
Specifications of traffic controller
Two street intersection
  Two sets of lights (green, yellow, red) for traffic towards the South and the West
One set of Pedestrian walk signals
  When the Pedestrian walk light is on, Southbound or Westbound traffic is not allowed to move (set their lights to red)
  Pedestrians could push the walk button for 2 seconds to request passage (suggested)
  Near the end of pedestrian allocated walk period, you must flash the don’t walk light to warn the pedestrians to hurry up (flashing frequency is up to you), you will need states dedicated to the toggle
  Don’t walk LED should be constantly on if you are not servicing pedestrian passage

## Slide 5
Specifications of Traffic Controller
Each traffic state should be held for 1-2 seconds (real time), this will be your delay value
If multiple sensors are pressed, make sure to service every request eventually
  E.g. if you are allowing Westbound traffic to go currently, and all 3 switches are pressed, you should service South/Pedestrian -> Pedestrian/South -> West
  The priority of service is arbitrary but make sure every requester is eventually allowed to go
If no switches are pressed, you may continue servicing the current state or cycle through the other stages (I suggest holding the state)

## Slide 6
Designing your hardware
Possible port combinations for the traffic lights and switches are in the lab manual
The southbound and westbound traffic will each have their own set of green, yellow, and red lights respectively
PF1 must be your do not walk light, and PF3 will be your walk light
The driver is a necessary component to interface all of your 6 LEDs with
There are three switches, two representing a sensor for southbound/westbound traffic and one for requesting pedestrian passage
I suggest using PB0-2 for your sensors, PE0-5 for your traffic lights, and of course PF1 and PF3 for your pedestrian lights

## Slide 7
FSM design tips
There will be multiple “duplicate” states (some states will have the exact same outputs as others)
  E.g. from the GoW state you can branch to WaitW > Pedestrian or WaitW > GoSouth
Minimum amount of states you need is 10, but to best handle all traffic scenarios, aim for 12-30 states (you will be graded on the flexibility of your software)
Think about what you want to do for each state when there are no switches, 1 switch, 2 switches or all 3 switches are pressed
Keep in mind that we want absolutely no traffic accidents, meaning only one street/the pedestrians may move at anytime
Each state will have a delay value, a PortF output and an output to whichever Port you decided to link your traffic lights to

## Slide 8
C TIps
The best way to organize your FSM is to create an array of structs (shown in class)
  Using this method, you will convert your sensor reading to an index for your next state
  E.g. state = (FSM[state].next_states)[sensor_reading]; //where FSM is an array of structs
Your structs are representing the states in your FSM
  Each struct will have components for traffic light output values, walk light output, and a delay time (as modeled when planning out your FSM)
  In addition, each struct will contain an array of 8 next states pointers/indexes (representing the transition arrows in your written FSM)
    There are 8 elements in this array because we have 3 inputs (2^3)
Use #define to create readable names for your next state indexes
  E.g. #define GoW 0, #define WalkS 12, and so forth
  You may also use address pointers instead (#define GoW &FSM[0], #define &FSM[12]) but make sure to access your structs in the proper manner if you choose to do so (this method is what I prefer, but conceptually indexing is easier to grasp in my experience).

## Slide 9
C Tips
When creating variables or constants, use clear and understandable names such as GoW, WaitW, sensor_reading, etc.
  Random variables such as x have no intuitive meaning to them and you will be penalized for style
Use SysTick_Wait10ms to implement your delays
  You must copy and paste SysTick.c and SysTick.h to your lab 5 folder in order to do so
  Add #include “SysTick.h” to the top of your main C file with the rest of the #include’s
  Right click the source directory at the left of Keil, add existing item, and add SysTick.c
  At the top of SysTick.c, remove the “inc/” in the #include “inc/tm4blahblah”
  Under SysTick_Wait10ms, change 500000 to 800000 (we are running at 80Mhz remember)
  Make sure to call SysTick_Init() along with the rest of your initializations

## Slide 10
example program flow
#define states as indexes or addresses
Create the struct
Create the array of structs
Initialize an index/pointer variable to access the elements of the array of structs
Initialize necessary ports and SysTick
Main loop
  Set traffic lights
  Set walk lights
  Delay
  Read sensors
  Update the array of structs index/pointer to the appropriate next state

## Slide 11
Deliverables
Combine all deliverables as a single PDF and commit them to Subversion
Logic Analyzer screenshot of the outputs/inputs when car are present in both lanes
Circuit diagram
FSM diagram, hand drawn or computer is fine
Any files/code you have added (most likely SysTick.c and SysTick.h) must be committed to SVN